Introduction

Alexander Hjelm, Visualization and Graphics at KTH.

This project has aimed to answer the technically feasibility of reconstructing a real-life city in 3D from OpenStreetMap road and building data. We will specifically focus on how feasible it is to generate pedestrian footpaths from OpenStreetMap data.

The idea of recreating real world cities in 3D applications has a growing number of applications, including visualization and modeling, urban planning and architecture, as well as media and entertainment in the form of video games and 3D animation.

The last decade has seen multiple startups in the area of procedural software for urban architecture, including ArcGIS Pro and CityEngine. Such software uses procedural models to render a city grid based on real-world locations, or generate new grids and features based on user-specified parameters, and allow for varying degrees of manual editing on grid, road, city block or individual feature level.

Even modern videogames use procedural methods for virtual city reproduction. In Cities Skylines you use an interface to define your own city grid and zoning constraints, and the program will generate a 3D representation of a virtual city that meets your requirements.

Whereas in Grand Theft Auto you navigate your avatar through a virtual city that has been premade, using assets by the game’s modelers and constraints made by the designers. Characters and cars in the game can plan out their own goals and use the larger city grid and finer details in the geometry to navigate.

Traditionally, modeling cities at this scale requires the use of procedural methods These are generative algorithms that rely on the availability of map data, which serves as the initial input to the procedure of model generation and placement. This can be any form of map features, from terrain to road networks and buildings, and are usually served as a list of polygons with points as world coordinates.

The problem is that software that replicates cities based on OpenStreetMap data is that they usually focus on replicating the OpenStreetMap data 1:1. Thus they do not account for errors in precision. Real world maps always have a maximum limit on their accuracy due to inaccuracies in measuring techniques. In the case of OpenStreetMap, where end users have contributed the large bulk of data, the data is often acquired by manual tracing features on other online maps such as Bing maps and Google maps. This means that the positional error in the OpenStreetMap dataset largely stems from the accuracy of satellite imagery, which is typically in the order of a few meters.

Why do we want to minimize the positional error? Here is a picture with bad examples from a 3D reconstruction of the Stockholm road map, with clearly visible geometric errors. You can see firstly a healthy intersection with main car roads, sidewalks and pedestrian crossings. Then a city segment where roads overlap with existing buildings, then a case where roads overlap with each other, and lastly an intersection where the road geometry twists and self-intersects in strange ways. These are all forms of error that can arise due to insufficient measuring precision. Apart from being disturbing in a 3D visualization context, they could also lead to inaccuracies in localization or path-finding methods.

It turns out that within this context, footpaths have a rather unique character. Walkways in parks appear to grow much more organically, and pavements form rough grid systems with organic branches that bridge over city blocks. Since very little research has been made in rendering footpaths in particular, I chose to focus on them specifically.

Geodata precision study

In order to find out how much leeway there is to correct collisions between features, our first goal is to obtain an estimate of the positional accuracy of the OpenStreetMap dataset. We will do so by looking at the distance between points of the same building’s representations in OpenStreetMap and a publicly available reference map from Svenska Lantbruksuniversitetet.

In the beginning, the completeness of the OpenStreetMap dataset was calculated. This is a measure of how many features are represented in both the OpenStreetMap dataset and the reference dataset, and was calculated as the relative difference in area of all building footprints. If two buildings were overlapping by more than 30%, they can be assumed to be the same.

The same area overlap function was used to find a mapping between buildings in OpenStreetMap and the reference dataset. This is not as straight forward as it may sound because feature representation might be different between the maps. They may have different policies for what buildings to include and how to subdivide larger buildings into plots. This type of semantic error means some buildings might not appear at all in either datasets, or some could be represented as many smaller buildings in the other dataset.

Once a matching set was found, a program took building pairs and extracted matching geometrical points after first creating simplified versions of the polygons that still retain information about the rough features, using the Douglas-Peucker algorithm. The idea behind Douglas-Peucker is to recursively divide a polyline. It refines the line segments of a polyline, and proceeds to do so until a line segment is found, where every point in between the endpoints have a distance to the line segment that is smaller than some resolution. All nodes in between the endpoints are discarded.

The next step is to obtain the OMBRs of the reduced polygons, and for both polygons find the edges that coincide with the edges of the OMBRs. These edges are corresponding, and thus their end vertices form a matching vertex map between the original polygons.

Finally, the average distance between all matching points was taken as a measure of the positional accuracy.

Adiitionaly, the shape accuracy of the OSM dataset has also been calculated as an extra verification of the similarity between the datasets. The shape accuracy relies on the polygon turning function that measures the cumulative angle of the polygon’s counter-clockwise tangent, as a function of the cumulative normalized length.

Overlap study

Once the positional error estimate was obtained from the precision study, it was used to assess the integrity of the OSM Stockholm road network Each road was assigned a standard width depending on its classification in OpenStreetMan, according to the Swedish Transport Administration.. Then a program located critical points where assigning standard widths to the roads would cause collision with other features, and then counted how many of those points could be eliminated by making adjustments within the found margin of error.

After the width assignment, a program calculated how many features that show overlap with any other feature, as well as the total length of the road that is intersecting some other feature. Finally, the program calculated how many of these colliding features that can be corrected by making adjustments that are within the positional accuracy of the OpenStreetMap data, as obtained by the geodata precision study.

Notes

For all methods that went over pairs of buildings, I used a prebuilt geometric hashmap. This speeded up calcluations considerably. Lay out a 2D grid and for every building, only step through the buildings or roads that fall in the same hash blocks as the one we are currently standing on. The key is that a building or road can be in several hash blocks.

Even so, the whole process took a good few hours on a normal laptop. Could be sped up by using a parallel computation environment where the calculations can be run on the GPU. The nature of the problem is easily parallelized since it consists of many small geometrical calculations of similar complexity that do not need write access to the source data. For the purpose of this project, only a sequential CPU solution was used since it yielded the necessary results in a reasonable timeframe. But for larger applications once should consider running a GPU-based solution.

Results

Positional accuracy study: average positional error of roughly 2 meters, as expected. This is compliant with previous OpenStreetMap quality studies.

For the collision study, the table shows the number of roads, number of edges and total edge length that showed intersections with other features. For footpaths in particular, it was shown that 12.05% of all roads collide with some other feature after extrusion to the minimum width. The same was shown to be true for 0.11% of the road polyline edges and 0.09% of the total road length. for the remaining roads, edges and total edges length whose intersections with other features could not be resolved by translation smaller than the positional accuracy. For footpaths this was shown to hold for 0.51% of all roads, and the number of road edges and percentage of the total road length was significantly small.

The area cover of the OSM buildings was about 98% of that in the reference set, and about 80% of all the buildings were mapped 1:1. For further calculations, the 1:0 matches were discarded and the 1:n matches were clustered together, and the minimum bounding suface taken as the new building.

The positional and similarity accuracies per building were plotted as frequency diagrams, and were fairly consistent to the findings of Fan et al.

By looking through cases of road overlap, I categorized them into 5 classes, but I will only mention them here. In the report you can find a detailed definition, and suggestions on algorithms to make corrections to each one that are within the positional accuracy of the map data.
Case 1: A building lies in parallel with a road, and the distance between the two is smaller than the minimum width of the road.
Case 2: A road shares a node with a building.
Case 3: A road is intersecting with certain building features.
Case 4: Two roads have a minimum distance that is smaller than the sum of the minimum widths of both roads.
Case 5: Two roads share a node, and a subsequent node in one road lies within the minimum width of the other road.

Conclusions

The primary conclusion of the footpath overlap study is that, in terms of feature overlap, footpaths were not significantly worse than other road categories. Thus it can very well be assumed that city modeling software could use the same routine for importing OSM car roads as well as OSM footpaths, with- out a drastic increase in feature overlap. The designer could build upon their existing procedure and add algorithms for overlap detection and correction.

Now we know the technical feasibility of importing an OpenStreetMap data slice and rendering the road network and buildings without intersections. The final contribution of this project was a scientific study into the possibilities of road network modeling in the broader context of 3D city reproduction. What are the remaining practical challenges for accurate 3D city reproduction? What techniques can be used to complement the basic system of importing street and building data that is already in place, and create a rich and living virtual city?

Remaining challenges

As has been mentioned in the introduction to this report, procedural generation of road networks is a basal requirement for quick and low-effort modeling virtual cities. Since the road network ties together the city, and forms the grid that divides the lots, quarters and neighborhoods, it make sense that one can only continue with the remaining challenges once there exists a robust procedure for extracting road geodata and generating the 3D representation of it without compromising the data integrity. The same is true for building modeling. As (Fan et al, 2014) notes, it turns out that the same methods that have been used in this project to obtain and qualify road network data can be applied to building footprint data from OSM. Only when there exists such a fundamental procedure for accurately importing building footprints without compromising the data integrity, one can proceed with the remaining challenges in building modeling.

Such challenges include inferring or guessing building height and including terrain elevation in the city model. Even if high resolution terrain elevation data is available from other sources, and sometimes even building heights, it is not provided by OSM, and will have to be obtained from a complementary data source, increasing the complexity of the problem. In some cases where an especially detailed city model is required, one might wish to include realistic textures for the building facades. This is typically done either by handpainting or photoscanning, which becomes a challenge since generally no photoset with complete coverage exists.

Feasibility in the urban planning field
For simple presentation in e.g. animation and video games or even urban planning software, proedurally enerated cities with generic 3D models could very well be enough. The big problem however is that these models will rarely match real life. They will be sufficient as long as one can be satisfied with looking at rough representations of buildings. However, many studies in urban development have been done before that required detailed knowledge about a city’s geometry, e.g. for the purposes of modeling traffic, crowd flow, heat development or reducing noise. Research in these field requires detailed morphological information that goes beyond simply knowing the geometry of the city. Urban architects often work with morphological structures where a single feature can be examined from many different perspectives. A neighborhood can be analyzed from the level of its city blocks, individual lots, building facades or even indoor spaces. Similarly a road network can be analyzed by looking at it either at its connectivity by viewing it a a simple 2D graph, but it might as well be seen as a hierarchical structure where primary roads branch off into sub-streets. A road can also be comprised of sections for different types of traffic. This type of representation is known as a multimodal structures, due to the possibility of incorporating multiple modes of transportation. The very unfortunate fact is that much of that morphological information is not present in OpenStreetMap. OpenStreetMap, while being an excellent source of city geometry, is simply not a sophisticated enough dataset to cater to all these possible areas of research. For media applications, such morphological and multimodal information could in theory be generated procedurally. But for urban planners requiring an exact morphological representation of some specification, this complementary data will have to be obtained from another dataset.

Final conclusions
The final conclusion is that generating virtual cities purely from OpenStreetMap data is perfectly feasible in the media industry, with the inclusion of procedural methods to generate necessary detail. This will be a cheap method that requires minimum effort and minimum data collection. The level of detail of the composition can be fitted to the scope of the project and the team size. However, in the area of urban design, urban planners often require complementary data to build morphological representations of the data that they are working with. OSM does generally not serve this type of data, so the feasibility of creating virtual cities that are of use to urban planners will depend on the availability of that complementary data elsewhere.